## Slide 1: Predicting NOx Concentration Level in Air
Malathi M
PGDM in Business Analytics,
REVA University, Bengaluru
Forecasting NOx Levels
May 2019

## Slide 2: Agenda
Problem Understanding
Data Gathering & Understanding
Data Preparation
Modelling
Interpretation
May 2019
Predicting NOx Levels

## Slide 3: Problem Understanding:
Overview on Air Pollution :
Air Pollution is one of the major environmental issues and becoming major health problem that are effecting millions of people worldwide. Exposure to pollutants for a long time can lead to premature deaths, asthma, lung cancer, heart attack.
Death by Contamination(as Reported by THE STRAITSTIMES)
May 2019
Predicting NOx Levels

## Slide 4
Impact of Air Pollution on economy:
As per OECD impact of outdoor pollution are projected to lead to global economic cost that gradually increase to 1% of global GDP by 2060
A World Bank Study shows that welfare costs and lost labour income due to air pollution amounted to 8.5% of India’s GDP in 2013
Problem Statement
To identify the pattern NOx of levels in air and building a predictive model to predict concentration levels of
NOx (Oxides of Nitrogen) and to know NOx levels are within AQI Index.
May 2019
Emission Projection over time (as Reported by OECD)
Predicting NOx Levels
Problem Understanding (Continued):

## Slide 5: Data Gathering:
Data Description:
Data Source : Central Pollution Control Board of India
Time Period : February 2009 to September 2018
Method : 4 hour Sampling
Variable | Variable Type | Unit of Measurement
NOx (Oxide of Nitrogen) | Pollutant | µg/m3
WS(Wind Speed) | Meteorological factor | m/s
WD(Wind Direction) | Meteorological factor | Degrees
VWS(Vertical Wind Speed | Meteorological factor | m/s
BP(Bar Pressure) | Meteorological factor | mmHg
Temp(Temperature) | Meteorological factor | Degree centigrade
RH(Relative Humidity) | Meteorological factor | Percentage
SR(Solar Radiation) | Meteorological factor | W/m2
Location and shape of the data
Location | Shape of the data
Kadubeesanahalli | 21126 observations & 9 variables
Peenya | 21360 observations & 6 variables
BTM Layout | 21006 observations & 9 variables
Description of the variables
May 2019
Predicting NOx Levels

## Slide 6: Data Understanding:
Distribution NOx at three locations :
May 2019
Most of the time since ten years the Nox levels are within the range of the AQI
Predicting NOx Levels

## Slide 7: Data Understanding(continued):
Classification of Concentrations levels as per AQI Index at three places
May 2019
Predicting NOx Levels
Yearly average concentration levels at the three places

## Slide 8
May 2019
Data Understanding(continued):
Predicting NOx Levels
Average concentration levels over weekdays
Hourly average concentration levels at every four hour time interval

## Slide 9
Seasonal Trend:
Peenya
Kadubeesanahalli
BTM
May 2019
Data Understanding(continued):
Predicting NOx Levels

## Slide 10: Data Processing:
May 2019
Predicting NOx Levels
Outlier Treatment
No specific treatment is done for outliers, dropped all the values below and above mean+/- 3*standard deviation.
Missing Value Replacement
No specific treatment is done for missing values, dropped all the missing values.
Splitting data
Creating test and train data at 75 and 25 ratio
At Kadubeesanahalli
At BTM
At Peenya
Missing Value Plot:

## Slide 11: Data Processing(Continued):
May 2019
Predicting NOx Levels
Data Size without 60 days lag as of NOx as independent variable |  |  |  |  |  |  |  | 
Location | Dependent Variable | Independent Variable | Data size before treatment |  | Data size after treatment |  | Train dataset | Test dataset
 |  |  | observations | variables | observations | variables |  | 
BTM | log(Nox) | BP,RH,SR,Temp, VWS,WD,WS | 21006 | 8 | 4323 | 8 | 3242 | 1081
Peenya | log(Nox) | BP,RH,SR,Temp | 21360 | 5 | 9995 | 5 | 7496 | 2499
Kadubeesanahalli | log(Nox) | BP,RH,SR,Temp, VWS,WD, WS | 21126 | 8 | 575 | 8 | 431 | 144
Data Size with 60 days lag as of NOx as independent variable |  |  |  |  |  |  |  | 
Location | Dependent Variable | Independent Variable | Data size before treatment |  | Data size after treatment |  | Train dataset | Test dataset
 |  |  | observations | variables | observations | variables |  | 
BTM | log(Nox) | BP,RH,SR,Temp, VWS,WD,WS,log(Nox) | 21006 | 8 | 3869 | 9 | 2901 | 968
Peenya | log(Nox) | BP,RH,SR,Temp, log(Nox) | 21360 | 5 | 8853 | 6 | 6639 | 2214
Kadubeesanahalli | log(Nox) | BP,RH,SR,Temp, VWS,WD, WS,log(Nox) | 21126 | 8 | 453 | 9 | 339 | 114

## Slide 12: Fitting and model Assessment:
May 2019
Predicting NOx Levels
Model Details | 
Sampling | Bootstrap – caret package (n = 1000 for stepwise regression)
Methods | Backward Elimination and Stepwise Regression
Validation | Loss/error on test dataset
Transformation | Log transformation of dependent variable
Model Details:
Model Details | 
Sampling | Bootstrap – caret package (n= 10 & 15)
Methods | Random forest
Validation | Loss/error on test dataset
Transformation | Log transformation of dependent variable

## Slide 13: Model Assessment(Continued):
May 2019
Predicting NOx Levels
Chart: PERCENTAGE VARIANCE EXPLAINED
| R2 | R2_lag | R2 | R2_lag | R2 | R2_lag | BTM | Peenya | KB
BWE | 19.63 | 38.52 | 8.763 | 22.76 | 61.72 | 61.87
Step | 19.1161 | 37.5774 | 8.6296 | 22.6476 | 58.199 | 58.8934
RF(n=10) | 64.63 | 65.02 | 27.97 | 37.56 | 73.05 | 73.72
RF(n=15) | 64.84 | 64.94 | 28.13 | 37.45 | 73.17 | 73.44
Chart: MAE for all three locations
| mae | mae_lag | mae | mae_lag | mae | mae_lag | BTM | Peenya | KB
BWE | 0.72109 | 0.59701 | 0.59842 | 0.51105 | 0.27022 | 0.22525
Step | 0.72113 | 0.5971 | 0.59842 | 0.51105 | 0.27022 | 0.22221
RF(n=10) | 0.43598 | 0.44421 | 0.51179 | 0.43166 | 0.21801 | 0.19422
RF(n=15) | 0.43751 | 0.44308 | 0.51106 | 0.43155 | 0.21802 | 0.19359
Chart: RMSE for all three locations
| rmse | rmse_lag | rmse | rmse_lag | rmse | rmse_lag | BTM | Peenya | KB
BWE | 0.96035 | 0.82425 | 0.37911 | 0.30901 | 0.86074 | 0.76441
Step | 0.96039 | 0.82439 | 0.37911 | 0.30834 | 0.86074 | 0.76441
RF(n=10) | 0.62813 | 0.65314 | 0.3367 | 0.29728 | 0.76604 | 0.69026
RF(n=15) | 0.63119 | 0.65248 | 0.33696 | 0.2947 | 0.76642 | 0.69097

## Slide 14: Model Interpretation:
May 2019
Predicting NOx Levels
Variable importance of random forest model for without and with lag variable:
Peenya
BTM
Kadubeesanahalli

## Slide 15: Model Interpretation(Continued):
May 2019
Predicting NOx Levels
Model fit for without and with lag variable:
Peenya
BTM
Kadubeesanahalli

## Slide 16: Recommendation:
May 2019
Predicting NOx Levels
Proper maintenance of the existing monitoring device.
Should increase the number of monitoring stations.
Peak hour traffic management to reduce pollutant emission due to traffic congestion.
Framing strong policies against emission of pollutant should be based on to the particular area based on the geography of the location.
Scope for improvement:
Time Series Analysis using RNN/LSTM

## Slide 17
May 2019
Predicting NOx Levels
Thank You!!